## Slide 1: Sound Effect Devices for Musicians: Synthesizer
Team: sdmay19-32
Members: Francisco Alegria,
Blake Beyer, Timothy Day, Eric Fischer, & Travis Gillham Advisors/Clients: Dr. Degang Chen & Dr. Randy Geiger
Notes: Talking: Travis

## Slide 2: Problem Statement
In today's world musicians can be put in a difficult spot with high cost of equipment. To address this challenge we set out to:
  Create a state-of-the-art synthesizer for an affordable amount
  Strive for major functionalities of a synthesizer
  Develop a graphical user-interface that wirelessly controls the system
Notes: Talking: Travis

## Slide 3: Solution
Analog voice synthesizer with digital controls & internal patch bay
Wireless user reconfigurable interface
Portable size
Low cost
Notes: Talking: Blake

## Slide 4: Functional Requirements
All modules function as expected
Interface changes with modifications to modules
Signal integrity is not degraded across the system
Notes: Talking: Travis

## Slide 5: Non-Functional Requirements
Performance
Security
Uses a predefined app over Wi-Fi which ensures the security of its data
Usability
The user interface of the device is a screen that modifies each one of the modules
Compatibility
Works with iPads, iPhones, and Android Phones
It was tested on an individual module basis and then all were combined
Notes: Talking: Blake

## Slide 6: Market Survey
Analog Synthesizers
  Bass Station 2 by Novation; Analog voice with digital controls $439
  Mother-32 by Moog; Semi-Modular patch bay, $599
  Grandmother by Moog; Semi-Modular with built in Spring Reverb Tank $899
Digital Synthesizes
  OP-1 by Teenage Engineering; Portable, Small built in screen, Multiple synth engines, $999
  OP-Z by Teenage Engineering; Ultra-Portable, User provided iOS screen, Multiple synth engines, $599
Software Synthesizer
  Massive by Native Instruments; PC/Mac only, can run multiple instances at once, $149
Notes: Talking: Blake

## Slide 7: Operating Environment
Studios
Live performances
Amateur home use
Notes: Talking: Eric
All depends on the musician.

## Slide 8: Deliverables
Contained within the housing are:
Oscillator
Low Frequency Oscillator
Mixer
Noise
Output Amplifier
Microcontroller with multiple I2C buses
Notes: Talking: Eric

## Slide 9: PCBS
Output Amplifier
Mixer & White Noise
Oscillator
Mixed Signal Modbay
Notes: Talking: Eric
Modbay and Oscillator PCBs were not used due to some faults in the design. Analog Modbay was used instead, and Oscillators were implemented on bread boards

## Slide 10: Implementation
Notes: Talking: Eric

## Slide 11: Proposed Design
Functional Decomposition
Notes: Talking: Paco

## Slide 12: Module Expectations
ADSR:
Applies envelope to output signal with the attack, decay, sustain, and release phases.
Filter:
User selects passbands.
Low Frequency Oscillator (LFO):
Sub audible oscillator for frequency modulation.
Mixer:
User selects attenuation for every input.
Noise:
Generates a white noise output.
Oscillator:
User selects generation of a sine, triangle, pulse, or saw output and a pitch offset.
Output Amplifier:
Controls output volume level.

## Slide 13: INTERFACE
Used to control all the synthesis modules as one complete system
Uses TouchOSC application for mobile devices; iPads, iPhones, and Android phones
Open Sound Control protocol to communicate via the Wi-Fi transceiver with the onboard microcontroller
The UI application also allows the user to instantly switch between multiple interfaces that are preloaded
Notes: Talking: Paco

## Slide 15: MICROCONTROLLERs
ARDUINO MEGA
Takes the data received from our interface and process it to set the internal control values
Sends data back to the interface to provide the user with feedback
Interprets the OSC data and communicates with the required components using the I2C protocol
Wi-Fi internet development board
Notes: Talking: Paco

## Slide 16: Housing
Gives user access to connect power rails and output speaker
Display shows the finished PCB designs
False floor covers breadboards for oscillators
The separated floors assist with wire management
Wood was selected as it doesn't block Wi-Fi signals
Notes: Talking: Tim

## Slide 17: Testing
Notes: Talking: Tim

## Slide 18: Testing Process & Validation
Module Concept
Schematic Design
Hardware Testing
Hardware Integration
Wi-Fi interface
Full Integration
GUI Development
Simulation
Breadboard
PERF Board
PCB
Meets validation and verification requirements
Notes: Talking: Tim

## Slide 19: Test CAse Validation
Noise Generator
Amplifies Avalanche breakdown of BJT
Validation Requirements
Voltage Output is 500mVrms
Voltage output is randomly distributed
Power Spectral Density distribution
  Mean & Standard deviation equal
  Gaussian Distribution
Audible Output that sounds like noise
Notes: Talking: Tim

## Slide 20: Final Device Functionality
Click to add text

## Slide 21: Conclusion
We were successful in creating a functional synthesizer from our own design
Some objectives where not reached
Learned numerous lessons along the way
  Diverse majors should be involved
  Development of a circuit design from start to finish
Notes: Talking: Tim

## Slide 22: Demonstration
Notes: Talking: Tim

## Slide 23: Thank you!